## Slide 1: Ternary Volatile Random Access Memory based on Heterogeneous Graphene-CMOS Fabric
  - Santosh Khasanvis, K. M. Masum Habib*, Mostafizur Rahman, Pritish Narayanan, Roger K. Lake* and Csaba Andras Moritz
  University of Massachusetts Amherst
  *University of California Riverside

## Slide 2: Outline
Motivation
Bi-Layer xGNR Device, Latch
Proposed Memory Cell - Ternary GNTRAM
Evaluation and Comparison with CMOS SRAM
Summary

## Slide 3: Multistate Memory: Motivation & Vision
Vision – New multi-bit per cell volatile memory with graphene
Challenges with CMOS SRAM
Slowdown in area scaling (50% down to 30% per generation)
Increasing leakage concerns
SRAM Area Trends
Source: 2012 ISSCC Tech Trends
Binary Memory Array
Current: Single bit/cell
Multistate Memory Array
Proposed: Multi-bit/cell with novel graphene structures
Concept
SRAM Cell Size

## Slide 4: Bi-Layer Graphene Nanoribbon Crossbar Device (xGNR) & Application
DC Load Line Analysis
Unstable
Stable
A
B
Graphene Nanoribbon Crossbar Resonant Tunneling Diode - K. M. M. Habib and R. K. Lake, University of California Riverside
xGNRs in series form a latch with multiple stable states (A, B & C)
Ternary data represented by state node (SN) voltage: A—Logic 0, B—Logic 1, & C—Logic 2
Armchair Graphene Nano-Ribbons arranged in a crossbar geometry (xGNR) exhibit Negative Differential Resistance (NDR)
DC Characteristics
Latch Configuration
Vdd
SN

## Slide 5: Graphene Nanoribbon Tunneling RAM (GNTRAM)
xGNR Latch
Memory Circuit
Proposed Memory Cell
xGNR latch forms the memory core of a RAM cell
Memory cell selection, read and write operations performed using access transistors
Schottky diode and Sleep FET mitigate stand-by power consumption

## Slide 6: Ternary GNTRAM Operation
Output
Write Operation:
  Ternary data represented by state node (SN) voltage
  Apply input voltage on ‘Data Line’ & assert ‘Write’ signal
  Charge/discharge state node to required voltage
Read Operation:
  Pre-charge ‘Data Line’ & apply ‘Read’ pulse
  Output is pulled down based on stored logic state
  Non-destructive read
Write Operation
Input
State Node
Input
Voltage
Read Operation
SN: Logic 2
SN: Logic 1
Read
Data Out
Simulation Time (s)

## Slide 7: Proposed Physical Implementation – Integration with CMOS
Heterogeneous integration between CMOS and Graphene for validation and benchmarking
MOS transistors and metal layers for access and routing
Schottky contact* enabled by interaction between semiconducting GNR and metal
Si MOSFETs
*X. Guan; et al.; , "Modeling of schottky and ohmic contacts between metal and graphene nanoribbons using extended hückel theory (EHT)-based NEGF method,“ IEDM 2008.

## Slide 8: Methodology & Benchmarking
HSPICE simulation for concept validation, performance and power evaluation
16nm Grid-based design rules used to evaluate GNTRAM area
 | GNT RAM (Per Cell, 1.585 bits) | GNT RAM (Per Bit) | CMOS 6T Scaled SRAM Cell | CMOS Gridded 8T SRAM Cell
RAM Cell Area (µm2) | 0.03-0.06 | 0.019-0.038 | 0.026-0.064 | 0.034-0.067
Active Power (µW) | 2.1 | 1.31 | 2.1 | 2.41
Standby Power (pW) | 22 | 13.9 | 6152 | 15552
Performance | GNT RAM | CMOS 6T Scaled SRAM Cell | CMOS Gridded 8T SRAM Cell
Read Time (ps) | 9.3 | 8.8 | 7.7
Write Time (ps) | 16.3 | 18.4 | 18
Comparison with 16nm High Performance (HP) CMOS SRAM
16nm Design Rules
Density Benefit (per bit) : Upto 1.77x vs. SRAMs
Power Savings (per bit): Upto 1.84x (Active) and 1196x (Leakage) vs. HP SRAMs
Performance: Comparable to HP CMOS SRAMs
C. Bencher, et al.. “Gridded design rule scaling: Taking the CPU toward the 16nm node”, Proc. SPIE 7274, 2009

## Slide 9: Summary
Novel ternary memory (1.5 bits/cell) presented with heterogeneous CMOS-Graphene implementation
Density and power benefits vs. 16nm CMOS SRAMs with comparable performance
Next Steps: Increasing number of states/cell – a new dimension for scaling
Possibility of all-graphene fabrics as graphene technology matures
Thank You!
Acknowledgements: Collaboration with Prof. Roger Lake, UC Riverside
Sponsors: